## Slide 1
Countdown Timer
UW-Stout Computer Engineering Program
CEE-345 Microprocessor System Design
Alison Zimmerman & Jacob Hillebrand with Dr. Cheng Liu
Abstract
The goal of this project was to create a countdown timer and stopwatch using the KL25Z development board, a 2x16 LCD, and a Digilent Keypad. The functionality will have a start, stop, pause, and resume for both the timer and stopwatch.
Source Code Snippet
Part List
Wiring Diagrams and Module Description
PMOD 16-Button Keypad
LCD Screen
Circuit Schematic
The following parts were used for the construction of ….
Quantity | Part | Cost
1 | 2x16 LCD Screen | $6
1 | Digilent Keypad | $10
1 | KL25Z Freedom Board | $31.11
1 | Potentiometer | $1
 | Total | $48.11
This 16-button keypad is able to take input from the user. It has 8 pins, 4 of which were used as inputs and the other 4 for outputs in this project. Rows are scanned for input using a 4x4 matrix.
The LCD screen consists of 16 pins. There is power, contrast, data, read and write, and a clock enable. The screen takes in 4 bits of coded binary to print characters a\up to 16 characters per line.
System Spec/Hardware Description
The brains of the operation is the KL25Z Freedom development board. The KL25Z has a 32-bit ARM Cortex M0+ processor that runs at 48 MHz. The GPIO on this board allows for control of peripheral devices, like the 2x16 LCD and Digilent Keypad.
Flow Chart
Final Design
void mode_select(void) {
  //Variables for use
  int not_done = 1;
  unsigned char key;
  //Print out instructions
  Clear_LCD();
  Print_LCD("A - Timer");
  Set_Cursor(0,1);
  Print_LCD("B - Stopwatch");
  //Pause for keypress
  while (not_done) {
  key = keypad_getkey();
  if (key == 'A' | key == 'B') {
  not_done = 0;
  }
  }
  //Based on keypress, take action
  switch (key) {
  case 'A’ :
  set_timer();
  timer_countdown();
  break;
  case 'B’ :
  stopwatch();
  break;
  default :
  break;
  }
}